## Slide 1
OPI-EVPN-BR Architecture
EVPN-GW offload to xPUs (Intel/Ericsson PoC)
Dimitrios Markou (Ericsson)
Feb 2024

## Slide 2: Agenda
Intel-Ericsson IPU PoC Overview
Network Architecture
K8s Tenant Networking and EVPN GW Design
  EVPN GW API (Already merged to OPI)
  Target Architecture
OPI-EVPN-Bridge Architecture
Sequence Diagrams
References

## Slide 3
Overview of the Intel-Ericsson IPU PoC
Working together on several IPU-based use cases :
  Telco edge networking for K8s
  remote manageability
  NW Security
Focus of the Networking use case
Supporting K8s primary and accelerated secondary networking – latter is critical for Telco use cases
An Integrated edge router (‘EVPN GW’) and managed underlay on the IPU
Building on open-source control planes on the IPU
Open architecture based on standard interfaces with goal to contribute vendor-agnostic code to the OPI community
Intel-Ericsson IPU POC Overview

## Slide 4: Network Architecture

## Slide 5: EVPN – Overlay and Network Separation
Datacenter
servers
Telco Edge or enterprise site
EVPN
L3/L2 VPN overlay
PE
PE
fabric
EVPN: Service Provider VPN technology standardized by the IETF ”BGP Enabled Services” working group (https://tools.ietf.org/wg/bess/)
Server with EVPN GW functionality on the xPU

## Slide 6: K8s Tenant Networking & EVPN GW Design

## Slide 7: EVPN Network Provisioning API
Lean API for EVPN orchestration
  Focus on essential entities and attributes for common use cases
LogicalBridge:
  Local L2 broadcast domain
  Optionally part of an L2-EVPN identified by L2 VNI
BridgePort:
  Attaches a VF to one or more LogicalBridges
  Access or VLAN trunk port
VRF:
  Local routing instance of an L3-EVPN identified by L3 VNI
SVI (Switched Virtual Interface):
  Connects a LogicalBridge to a VRF for L3 VPN connectivity
automatically managed by xPU Infra Manager and FRR

## Slide 8: Tenant Networking & EVPN GW offload – Target Architecture
Host
K8s pod
xPU
ARM Cores
VRF routing
VXLAN encap/decap
VLAN-aware L2 Bridge
K8s Control Plane
EVPN Gateway CP (FRR)
Kubelet
EVPN GW CNI
OPI-EVPN-BR
IPSec CP
(strongSwan)
K8s pod
eth0
Secondary access VF
Control plane interface
Data plane fast path
Vendor SDK
Primary VF
Primary CNI
KubeProxy
Linux routing iptables
Data plane slow path
IPSec encryption/decryption
Linux Bridging & Routing CP and slow path
Network Provisioning CLI (godpu)
Vendor Plugin
Vendor Agnostic
Upstream Target
Vendor Specific
Existing Open Source
Plugin
Underlay routing
Secondary trunk VF
EVPN GW gRPC API
Programmable HW pipeline

## Slide 9: OPI-EVPN-Bridge Architecture

## Slide 10
CLI
EVPN-GW API
gRPC Server
Translation
Object Store
Storage Library
Set ()
Get()
List()
….
DB
Task Manager
Linux (SlowPath)
General Linux Mod
Vendor Linux Mod
FRR Mod
Subscriber Framework
Vendor Mod
FRR
Netlink Watcher
FastPath
InfraDB
notify
ApplyConf
PollConf
notify
Subscribe
opi-evpn-bridge core
Vendor provided
SlowPath
Offload
Vendor choice

## Slide 11: Flexible modular design
IPU
xPU
CI
Linux General Module
Linux IPU Module
FRR Module
Netlink Watcher
IPU Offload Module
Linux General Module
Linux xPU Module
FRR Module
Netlink Watcher
xPU Offload Module
Linux General Module
Linux CI Module
FRR Module

## Slide 13: Sequence Diagrams
Create VRF example
Netlink Module (VRF example)
Requeue Failed Task
Resiliency

## Slide 14: References
OPI-EVPN-BR
EVPN-GW-API
GoDPU
EVPN-GW-CNI

## Slide 15: THANK YOU!

## Slide 16: Backup

## Slide 17: EVPN Control and Data Plane
Datacenter
PE
PE
servers
EVPN uses BGP in the control plane and VXLAN in the data plane. We use additional IPSec encapsulation for security.
BGP session
VXLAN/IPSec tunnel
BGP session
fabric
VXLAN/IPSec tunnel
EVPN implementation
Server with EVPN GW functionality on the xPU
Telco Edge or enterprise site

## Slide 18: Network scenario
Datacenter
Arbitrary IP transport
PE
PE
fabric
servers
Telco Edge or enterprise site
Server with EVPN GW functionality on the xPU
Telco Edge or enterprise site
Server with EVPN GW functionality on the xPU
Telco Edge or enterprise site
Server with EVPN GW functionality on the xPU
EVPN GW functionality = Edge router with integrated routing and bridging
Arbitrary IP transport
Arbitrary IP transport
Arbitrary IP transport
Arbitrary IP transport
Goal: Optimize stand-alone server (and small cluster) deployments on telco edge and enterprise edge sites: Avoid CAPEX for dedicated site network equipment and remove dependencies on transport infrastructure

## Slide 19: EVPN routing
Transport network
Host
xPU
…
Tenant network bridge
Underlay routing
K8s pod
K8s pod
K8s pod
K8s pod
IPSec
VPN
VRF
VPN
VPN
VPN
VRF
VRF
VRF
GRD
Host
xPU
…
Tenant network bridge
Underlay routing
K8s pod
K8s pod
K8s pod
K8s pod
IPSec
VPN
VRF
VPN
VPN
VPN
VRF
VRF
VRF
GRD
GRD routes
VPN routes
BGP EVPN
Site 1
Site N